## Slide 1: LEGO
Maddy Selby
Dogbone of the Week
March 9, 2023

## Slide 3: LEg GOdt
1932 – Ole Kirk Kristiansen makes wooden toys in Denmark
Mid-1930s – they buy a milling machine!
1936 – company name meaning “play well”
Notes: Cars, airplanes, yoyos, ladders ironing boards, etc

## Slide 4: Moving to Plastic
1946 – first plastic injection moulding machine
1949 – Automatic Binding Bricks
  Poor interlocking quality
1951 – Ferguson Tractor is top selling plastic toy
1955 – LEGO System in Play
1958 – LEGO System is the only plastic toy

## Slide 5: The real LEGO bricks
LEGO bricks patent filed in 1958
Stud and tube coupling

## Slide 6: Materials
Originally cellulose acetate (based in wood)
  Tendency to warp severely
  Doesn’t hold color over time
1963 shift to ABS
  Better molding precision
  Accuracy 1/200 mm
  Relatively inexpensive
  Colorfast

## Slide 7: Manufacturing
1961 Hot Runner mold
1965 vacuum molding
Early 1970s thermoforming

## Slide 8
ABS (Acrylonitrile Butadiene Styrene)
Hard plastic
Scratch resistant
Easily moldable
HIPS (High Impact Polystyrene)
Strong
Tough
SEBS (Styrene-Ethylene-Butylene-Styrene)
Soft
Elastic
Behaves similar to rubber
LEGO makes the most tires per year!

## Slide 9
PA (Polyamide)
Absorbs high loads and impacts
MABS (Methyl Methacrylate-Acrylonitrile-Butadiene-Styrene)
Transparent
Not as strong as ABS
PC (Polycarbonate)
Strong
Impact resistant

## Slide 10
POM (Polyoxymethylene)
Stiff
Flexible
Strong
Dimensional stability
PE (polyethylene)
Soft
Durable
Flexible
Made from sugarcane!!

## Slide 11: Manufacturing Process Today
Plastic Granulate
Heated to about 230°C
Forced into the mold at up to 29 ksi
Notes: 3:08-3:18

## Slide 13: LEGO House
3.5 million bricks!!
3800 hollow blocks
272 bricks each
12 x 6 x 8 bricks

## Slide 14: Inside the LEGO House

## Slide 15: Why Can’t We Realistically Build a House Out of LEGO Bricks?
Held together with a snap fit
  Friction dependent
Under tension, they want to separate
But, good in compression
  2x2 brick withstood 4240N
    Equivalent of 375,000 bricks stacked on it
    2 mile high tower
Good in shear also

## Slide 16: Why Can’t We Realistically Build a House Out of LEGO Bricks?
Not really cost effective
A masonry brick costs $0.65
The LEGO House cost roughly $350,000 in just LEGO bricks